## Slide 1
Spectrum Data
Data Separation
Data Classification
1D-CNN Training (deep leaning)
Prediction (with model)
Comparison with AI and Worker
Interpolation and integration
1. 목적 : Raman Spectrum으로 부터 Nano plastic 성분 정량화
Measurement  Raw data
Raw data  Data Separation
Peak “o” or “x”
Deep leaning (param. Layer, Neuron, Epoch, Validation split…)
Train Loss & Accuracy, Test Loss & Accuracy
Compare the two resulting values, and use the corrected
Quantify based on classified results

## Slide 2
2. Spectrum Data
Raw data file의 data frame.
Header // 1열 : X, 2열 : Y, 3열 : Wavelength,
1열 : x axis. , 2열 y axis (Mapping), 3열 이후 Intensity

## Slide 3
3. Data Separation
Raw data file의 data frame.
Header // 1열 : X, 2열 : Y, 3열 : Wavelength,
1열 : x axis. , 2열 y axis (Mapping), 3열 이후 Intensity

## Slide 4
4. Data Classification
분류 과정에 대한 프로그램 작성

## Slide 5
5. 1D-CNN Training (deep leaning)
Model Summary
Using device : cuda  GPU 사용
레이어 구성
  Input size : 1336
레이어별 분석
  Linear-1 : Fully connected layer
  1336 에서 128로 변환
    Param. 1336 x 128 +128 = 171136
  ReLu-2 : 출력값에 비선형성 추가
  Dropout : overfitting 방지
  …
  Sigmoiud-11 : Normalize 함수 (이진 분류 목적 설계)
Input size : 1336
1336  128  64  32  1
Layer1
2
3
4
[0, 1]
Data ex) [0, 0.1, -0.1 …. ]
Model 최적화 중…

## Slide 6
5. 1D-CNN Training (deep leaning)
Training GUI
Param. 설정에 따라 다르지만, 사용하는 컴퓨터에서 대략 30분 정도 소요됨.
Pytorch 사용

## Slide 7
6. Prediction (with model)
Training 된 모델을 결과로 Peak 유무 예측
Best accuracy, Total count, positive negative count …

## Slide 8
7. Comparison with AI and Worker
사람이 분류한 작업 결과
1D CNN 예측 결과
두 결과 값 비교하여 Report 작성

## Slide 9
8. Interpolation and integration
plt.title('Linear Interpolation') plt.title('Polynomial Interpolation') plt.title('Gaussian Fitting') plt.title('Savitzky-Golay Filter') plt.title('Fourier Transform') plt.title('Moving Average')
Param. : Length, polynomial order
아직 프로그램 상 구현은 안됨.
여러 옵션을 적용해 볼 예정

## Slide 10: Raman spectrum Model update & Interpolation
2025. 02. 03
Lee Jeong-su

## Slide 11
1. Model update
M4 |  |  |  |  |  |  |  | 
 | small ng samp 4 | small ng samp 5 | small ng samp 6 | small ng samp 7 | small ng samp 8 | small ng samp 9 | small ng samp 10 | Sum
Matching_count | 390 | 379 | 385 | 396 | 379 | 373 | 388 | 2690
Non_matching_conut | 10 | 21 | 15 | 4 | 21 | 27 | 12 | 110
Non_matching_peak_1_count | 10 | 21 | 15 | 3 | 20 | 24 | 12 | 105
Non_matching_peak_0_count | 0 | 0 | 0 | 1 | 1 | 3 | 0 | 5
Total_count | 400 | 400 | 400 | 400 | 400 | 400 | 400 | 2800
Matching rate | 97.50% | 94.75% | 96.25% | 99.00% | 94.75% | 93.25% | 97.00% | 96.07%
M5 |  |  |  |  |  |  |  | 
 | small ng samp 4 | small ng samp 5 | small ng samp 6 | small ng samp 7 | small ng samp 8 | small ng samp 9 | small ng samp 10 | Sum
Matching_count | 394 | 380 | 393 | 398 | 381 | 381 | 389 | 2716
Non_matching_conut | 6 | 20 | 7 | 2 | 19 | 19 | 11 | 84
Non_matching_peak_1_count | 6 | 20 | 7 | 2 | 19 | 14 | 11 | 79
Non_matching_peak_0_count | 0 | 0 | 0 | 0 | 0 | 5 | 0 | 5
Total_count | 400 | 400 | 400 | 400 | 400 | 400 | 400 | 2800
Matching rate | 98.50% | 95.00% | 98.25% | 99.50% | 95.25% | 95.25% | 97.25% | 97.00%
Chart: 
| small ng samp 4 | small ng samp 5 | small ng samp 6 | small ng samp 7 | small ng samp 8 | small ng samp 9 | small ng samp 10 | Sum
M0 | 0.8725 | 0.805 | 0.84 | 0.9775 | 0.9225 | 0.875 | 0.78 | 0.8675
M1 | 0.9275 | 0.8475 | 0.905 | 0.9925 | 0.9225 | 0.935 | 0.87 | 0.91429
M2 | 0.95 | 0.885 | 0.885 | 0.995 | 0.9075 | 0.9225 | 0.905 | 0.92143
M3 | 0.9725 | 0.89 | 0.945 | 1 | 0.91 | 0.9225 | 0.95 | 0.94143
M4 | 0.975 | 0.9475 | 0.9625 | 0.99 | 0.9475 | 0.9325 | 0.97 | 0.96071
M5 | 0.985 | 0.95 | 0.9825 | 0.995 | 0.9525 | 0.9525 | 0.9725 | 0.97
M0 : CNN 초기 모델
M5 : CNN 최신 모델
Matching rate : 97% (M5)
SUM
Samp10
Samp9
Samp8
Samp7
Samp6
Samp5
Samp4

## Slide 12
2. Interpolation and integration
Setting
  Fourier Transform
  Savitzky-Golay
Fourier Transform
  Freq. Cutoff
Savitzky-Golay Fliter
  Window_length
  Polyorder
Linear interpolation
  Center wavelength
  Span
Interg. Val.  Quantification with Cal.